## Slide 1: Absorption Corrections in MANTID
22nd June 2018

## Slide 2: Available Algorithms
Numerical integration with just sample:
  FlatPlateAbsorption
  CylinderAbsorption
  AbsorptionCorrection: any shape defined using CreateSampleShape
Shared code to compute integral based on path lengths
Difference is just how paths are computed initially and slightly easier interface for defining the shape

## Slide 3: Available Algorithms
Monte Carlo:
  MonteCarloAbsorption: generic shape including optional sample environment
  AnnularRingAbsorption: cylindrical sample in the wall of a hollow can
AnnularRingAbsorption uses generic monte carlo technique under the hood but provides a simpler interface for defining the shape

## Slide 4: Available Algorithms
Specific algorthims:
  HRPDSlabCanAbsorption: Takes into account vanadium windows at front/rear of sample and aluminium holder (uses FlatPlateAbsorption to compute sample correction)
  PearlMCAbsorption: Loads pre-calculated files for Pearl’s complex geometry

## Slide 5: Comments
All algorithms have been in use for quite some time and are well verified
The AnnularRingAbsorption algorithm has some performances issues due to it using the underlying generic shape monte carlo code to do the work – this should not be an insurmountable challenge to solve