## Slide 1
Background Several imaging instruments are currently being constructed at neutron sources around the world, including IMAT1 at the ISIS facility, VENUS at the SNS and ODIN at the ESS. IMAT (Imaging and Materials Science & Engineering) will begin its scientific commissioning phase in Autumn 2015, and has several unique software requirements to control the data reduction and analysis of its imaging data. The Mantid software project2 provides an extensible framework that supports high-performance computing for data manipulation, analysis and visualisation of scientific data3. The Mantid framework is mature and widely used across many facilities and techniques. It is being extended to provide specific support for neutron imaging requirements. Being part of the Mantid framework, the software introduced here effectively integrates with a vast array of capabilities and methods readily available in Mantid. Mantid is open source, supported on multiple platforms (Windows, Linux, Mac OS X), and packages are available for easy deployment. Frameworks Here we introduce the imaging functionality that is being integrated in Mantid. A new custom graphical user interface integrates reconstruction and visualisation capabilities for neutron imaging. This interface gives access to new features of Mantid to load images and stacks of images into standard Mantid data structures and process imaging data. It also provides access to third party software such as packages for tomography reconstruction that support different 3D image reconstruction approaches. Mantid has the capability to run image reconstruction jobs either locally or in compute clusters and supercomputing facilities thereby enabling quick evaluation and refinement of the reconstruction pipeline. Compute resources Within ISIS, the SCARF and Emerald clusters, administered by the Scientific Computing Department at STFC, will allow rapid refinements during the imaging experiments. A key hurdle is the ability to take full advantage of available computing resources. Different facilities frequently choose different job scheduling tools, interfaces and hardware for their computing resources. For example the SCARF cluster at ISIS uses Platform LSF, while the clusters at the SNS use MOAB. The Mantid framework provides the middleware required to control jobs in different computing facilities handling the different job schedulers and/or web service interfaces. The Mantid framework itself can be used through its scripting interface via a web service API. This addresses challenges that arise at different facilities, such as different authentication methods, job schedulers, and location of compute resources. It also enables users to take full advantage of CPU and GPGPU clusters. At ISIS, users of the IMAT instrument will benefit from the high performance computing services provided by the ULTRA platform. | Tomography: reconstruction tools The imaging interface being integrated in Mantid supports third party software for 3D image tomographic reconstruction. A number of tools are currently supported and/or being trialed: TomoPy4, Astra Tomography Toolbox5, and Octopus6, and in the future the reconstruction pipeline software Savu7 developed by the Diamond light source. Different reconstruction approaches are thus supported, namely filtered back projection and iterative methods such as simultaneous iterative reconstruction technique, but also variants of these developed in different tools. Mantid also integrates multidimensional visualisation tools that leverage on the VSI (Vates simple interface) and ParaView8, providing powerful tools to visualise the ≥4 dimensional data that can result from imaging at a time of flight spallation source. | Pre-/post-processing and visualization Future Mantid and its imaging features are being actively developed. Long-term objectives include dealing with the multiple challenges posed by the complex datasets with three or more dimensions produced by energy-dependent tomography experiments: data volumes, better tailored pre-/post-processing, ease of analysis, etc. Equally important is aiding our users through the process of building their analysis workflows using the new features, and extending the tools on both the visualisation and manipulation and analysis sides where needed. References [1] W. Kockelmann, S.Y. Zhang, J.F. Kelleher, J. B. Nightingale, G. Burca,, J.A. James, (2013). IMAT – A New Imaging and Diffraction Instrument at ISIS, Physics Procedia, 43: 100-110 . [2] www.mantidproject.org [3] O. Arnold, et al., (2014). Mantid—Data analysis and visualization package for neutron scattering and μSR experiments, Nuclear Instruments and Methods in Physics Research Section A, 764(11): 156-166. [4] Gürsoy D, De Carlo F, Xiao X, and Jacobsen C, (2014). TomoPy: a framework for the analysis of synchrotron tomographic data. Journal of Synchrotron Radiation, 21(5):1188–1193. [5] W. van Aarle, W J. Palenstijn, J. De Beenhouwer, T. Altantzis, S. Bals, K. J. Batenburg, and J. Sijbers, (2015). The ASTRA Toolbox, a platform for advanced algorithm development in electron tomography, Ultramicroscopy, 157: 35–47. [6] octopusimaging.eu [7] R. C. Atwood, A. J. Bodey, S. W. T. Price, M. Basham, M. Drakopoulos, (2015). A high-throughput system for high-quality tomographic reconstruction of large datasets at Diamond Light Source, Philosophical Transactions A, 373(2043): 20140398. https://github.com/DiamondLightSource/Savu [8] www.paraview.org
Federico Montesino Pouzols1, Nicholas Draper2, Sri Nagella3, Erica Yang3, Ahmed Sajid3, John Hill1, Genoveva Burca1, Triestino Minniti1,4, Winfried Kockelmann1,
1 ISIS Pulsed Neutron and Muon Source, Rutherford Appleton Laboratory, Science & Technology Facilities Council – STFC, Harwell Oxford, OX11 0QX, UK
2 Tessella Ltd, Abingdon, Oxfordshire, OX14 3YS, UK
3 Scientific Computing Department, Science & Technology Facilities Council - STFC, Harwell Oxford, OX11 0QX, UK
4 CNR-IPCF, Viale Ferdinando Stagno D’Alcontres, n. 37 – 98158, Messina, Italy
Neutron imaging data processing using the Mantid framework
The new imaging features of Mantid are being tested with simulated and sample images. Mantid provides a harmonised and simple interface to different, heterogeneous tomographic reconstruction methods and tools which provide a varying degree of support for image pre-processing tasks.
Mantid is being extended with support for several input/output formats and additional parameterization and pre-/post-processing functionality. Several pre-processing tasks that are essential for effective tomographic reconstruction are being integrated in a harmonised manner, considering different forms of image normalization, filtering and selection of regions of interest.
Example image (top: single energy band, bottom: average across multiple energy bands) taken for testing purposes with the IMAT MCP detector, on a test beamline at ISIS.
Interface for the submission and control of remote reconstruction jobs. Multiple jobs can be submitted simultaneously, using common and specific parameters, and taking full advantage of the compute resources available on site for rapid in-experiment analysis and also off-site data analysis.
Mantid imaging interface integrated in the general Mantid graphical user interface with functionality for general manipulation and analysis of neutron data. Support is being added for different data formats (NeXus NXtomo, FITS, TIFF, PNG, etc.) and variants of them, as well as extensions currently being defined for more specific processing of imaging data from IMAT.
Section of the imaging interface for selection of different image parameters, including center of rotation, regions of interest, normalization region (white beam).
Simplified system architecture of the project ULTRA2 (Ultra High-throughput HPC Platform for Scientific Applications). This project, led by the Scientific Computing Department at STFC, aims at providing secure and efficient high performance computing and data services to support operations at ISIS and the Diamond Light Source. Mantid is capable of using ULTRA2 high performance computing services in a way that is transparent to the user, via a standardized web service.
Remote compute resource settings in the imaging interface of Mantid, including parameters and user credentials for remote execution of reconstruction jobs on a HPC platform.
SCREENSHOT NEEDS UPDATE,
BUT APPROX SOMETHING LIKE THIS