## Slide 1: Multiple scattering
ISIS Mantid Scientific Steering Committee
Break-out session
Anders Markvardsen, ISIS Facility, June 2018

## Slide 2: Agenda
What multiple scattering support is available via Mantid
What has been tested
What is missing
Discussion and questions

## Slide 3: Code within Mantid
Incoherent (vanadium) and cylinder geometry
  MayersSampleCorrection
  MultipleScatteringCylinderAbsorption : Carpenter (faster than above)
    Recently changed name to CarpenterSampleCorrection
Flat and Cylindrical geometry general S(Q,w)
  MuscatSofQW
  Old FORTRAN, not even understandable by Spencer or others who have attempted
    Trusted by a few users
    Available from Windows in Mantid
  VESUVIO
    VesuvioCalculateMS
    J Mayers (check) code translated
    No geometry
    Specific to VESUVIO
Notes: Mayers performs the integration for attenuation of a single scattered neutron and then simulates a load of second scattering events to produce a ratio between second and first order scattering which is then assumed constant between orders
MSCA uses power series approximations for both corrections
Only noticed Muscat this week, not had much time to look at it. Written in FORTRAN. Will mention this again in relation to McStas

## Slide 4: Support through other software
LoadMcStas

## Slide 5
http://docs.mantidproject.org/nightly/algorithms/LoadMcStas-v1.html
Notes: Take instrument design one step further
Pre-experiment analysis
Multiple scattering for general geometries?

## Slide 6: General expectation…?
For where speed and frequency is important
  Need for code within Mantid higher
Where the above less important
  Stronger case for interfacing with existing multiple scattering supporting software than replicated existing software functionality

## Slide 7: What MS support does McStas have on offer
Single component (e.g. the sample)
  Any geometry
  Powder/single crystal S(Q)
  Isotropic S(Q,w)
  Experimental code for general S(Q,w)
Any combination of components (called Union in McStas)
  Each item any geometry
  Powder/single crystal S(Q)
  Incoherent scatter (e.g. Vanadium)

## Slide 8: Status of the McStas sample components, sep 2015

## Slide 11: What has been tested

## Slide 12: Investigation Mantid/McStas multiple scattering against vanadium
Report by summer student James Tricker 2017: https://github.com/mantidproject/documents/blob/master/Presentations/Multiple%20Scattering%20Presentation/Investigating%20multiple%20scattering%20with%20McStas.docx
-> Note, all/most shortcomings discussed in report have been addressed since he left

## Slide 13
Notes: Since both separate the correction into two factors, absorption and multiple scattering, decided to test the absorption correction first. Preexisting analytic algorithm cylinder absorption (CA) well trusted by Mantid, been tested in other cases and been tested against similar Monte Carlo algorithms. Mayers quite grainy especially zoomed in. Could increase integration steps. MSCA slanted. Assumes out of plane scattering.

## Slide 14: Full comparison
Notes: Simply divided the two algorithms. Apart from scaling factor and slight slope due to cylinder absorption correction differences the algorithms seem to agree which is reassuring considering they use different methods to calculate the correction.

## Slide 15: Vanadium testing with McStas and Mantid
Notes: Ran a simulation with a cylindrical sample of vanadium and split the output into a single and all workspace. Applied the corrections to the All workspace and also did a cylinder absorption correction on the single workspace to get rid of any attenuation effects to give us a comparison workspace called Ideal.

## Slide 16: Other testing: McStas
isotropic_sqw by Emmanuel
Union geometry with diffraction and incoherent components by Mads
At ISIS cloud/Linux instant with McStas/Mantid setup – waiting for a volunteer with time!

## Slide 17: Other testing: McStas – Mantid interface
As originally agreed with members of the ISIS spec group: Cloud/Linux instant with McStas/Mantid available and ready – just waiting for a volunteer with time!

## Slide 18: Going back to the agenda of this meeting
What multiple scattering support is available from Mantid
What has been tested
What is missing
Discussion and questions