## Slide 1
Background Large neutron scattering datasets are commonly collected at time-of-flight (TOF) sources, particularly for single crystal diffraction experiments. A full understanding of the materials of interest often requires the complete mapping of data in an n-dimensional manifold. Increasingly, and particularly in single crystal diffraction (SCD), the correct treatment of data as part of data reduction and analysis, for a range of techniques, involves the efficient and flexible processing of large n-dimensional datasets. A collaborated effort involving ISIS at RAL, the SNS at Oakridge, and more recently the ESS in Lund, has focused on the computational aspects of single crystal diffraction data processing. Frameworks Mantid is an extensible framework for neutron and muon data reduction and analysis1. The Mantid framework is mature and widely used across many facilities and technique areas. For n-dimensional visualisation, the Mantid project uses ParaView2, an advanced VTK based visualisation engine. Mantid bundles a lean distribution of ParaView with each install. Mantid binds to ParaView via the introduction of multidimensional data structures and algorithms. In addition, we utilise ParaView’s plugin mechanism to provide customised tools for neutron scattering. We also deliver two-way interaction between ParaView and Mantid so that users can visually drive the data reduction and analysis processThis has required engineering and innovations on both the Mantid and VTK side of the project. Data Structures Mantid stores it’s data in structures known as Workspaces. Converting from TOF, detector-space to reciprocal space, as well as the need to consider sample environment conditions space has required the introduction of new Workspace types. Two multidimensional workspace types have been introduced: A sparse workspace, based on an adaptive box structure, and a dense histogram workspaces based on a set of strided arrays. Both workspace types are necessary for SCD computations in Mantid. Our sparse workspace stores all observations in the specified dimension. These are stored in a tree structure to allow fast access. Crucially there is a dynamically determined structure, this means regions of low counts have a very low memory overhead, while regions where constructive interference has occurred have a very fine and detailed structure. This workspace has been important for many reasons. Having full and fast access to the observations allows to dynamically rebin, which we do as part of many of our visualisation tools. Dense regions of the adaptive structure are easy to find, and indicate the presence of features, we therefore use them in algorithms. The dynamic structure also provides a good first-pass visualization. | Algorithms A key hurdle is the ability to identify peaks, which we can do automatically. We use a hierarchical, recursive data structure, to store our n-dimensional data, which is particularly effective, as it gives higher resolution in the regions of the Bragg peaks at an overall low memory cost. UB matrix finding and optimisation functions are now well established. We have adapted, and built upon concepts from the ISAW3 framework using specialist knowledge from that team. We have worked extensively on the problem of SCD peak integration. Our initial work in this area started with spherical integration, using fixed radii in Q to sample the peak area as well as a background region for normalization. More recently we have introduced an elliptical integration in Q, which determines a principle and secondary set of axis for each peak by finding corresponding Eigen vectors. Our latest introduction uses an imaging technique, connected component analysis, to integrate arbitrary peak shapes. Normalization The quantity of interest is the differential scattering cross section ds/dW, not the neutron count. However, eager normalization prevents correct summation of multiple scans. correctly normalizing and summing data from multiple experimental means tracking and separating the counts separately from the flux and solid angle contributions from each detector. Our solution is to calculate and sum the flux and solid angle contributions to each bin in reciprocal space across all scans, which we designate our normalization workspace. The counts for each run can then be summed and divided by our normalization workspace. The process of generating the normalization workspace can be expensive as we need to calculate the integrated flux between two wave vectors for every trajectory passing through a bin in our reciprocal data space. We have applied optimizations to the algorithms to improve speed and reduce memory. Our computed normalization workspace also acts as a planning tool, and we can use it to design experiments prior to beam time. | Visualization Visualization in Mantid provides a means to scrutinize the data and data treatment. We provide different levels of visualization brining the user from the quantitative 3D/4D projections all the way down to qualitative 1D linear cuts. All of the these tools cater for the possibility of in-situ rebinning and can drive the analysis as well as passively observe changes to underlying data. As well as providing full dataset visualization via VTK, a well used tool is our SliceViewer, which allows users to take 2D projections through nD datasets and extract 1D slices both graphically and programmatically. Our visualization tools are connected, so it’s possible, for example, to launch the SliceViewer(2D) from a region of interest on a 3D/4D dataset. The SliceViewer gives us the ability to stack multiple peak lists over the same reciprocal space and edit them independently if needed. Future Mantid is actively being developed. Frequent meetings with instrument scientists continue to provide a steady stream of additional requirements and challenges. A large number of Mantid’s current SCD suite is based on computations in reciprocal space. However, Mantid does not inherently assume either dimensionality or units for it’s data. We can therefore easily extend the suite to include other methods. We intended to do so to incorporate other proven peak integration routines. New developments in hardware lead to higher data rates. The introduction of the ESS into the collaboration will yield challenges to our existing methodologies. References [1] www.mantidroject.org [2] www.paraview.org [3] Worlton, T. G., Bouzek, C., Chatterjee, A., Hammonds, J.P., Mikkelson, D.J., Mikkelson, R.L., Miller, M., Peterson, P.F. and Serum B. (2004) New Software for Neutron Scattering Data Visualization. Neutron News 15(3), 14-15.
Owen Arnold1, Nick Draper1 Pascal Manuel2,
Andrei Savici3, Anton Piccardo-Selg1, Martyn Gigg1, Steven Hahn3, Vickie Lynch3, Alex Buts2, Peter Peterson3, Stuart Campbell3, Toby Perring2,
1 Tessella, Abingdon, Oxfordshire, UK
2 STFC Rutherford Appleton Laboratory, Oxfordshire, UK
3 Oak Ridge National Laboratory, Oak Ridge, Tennessee, USA
Visualisation and Analysis in Mantid for Single Crystal Neutron Diffraction
Elliptical peak integration of TOPAZ data. Right is zoomed version of left. Full data reduction and 3D visualization performed in Mantid.
Sparse data workspace schematic
TOPAZ measurements in 11 different orientations correctly normalized.
Left: Slice through an multi-dimensional workspace in Q-lab. Algorithmic output fed into visualization to show spherically integrated regions. Right: 3D representation of integration regions with Bragg peaks in Qlab. Both from cublic NaCl on SXD.
Editing auto generated peak lists interactively in the SliceViewer. Instantaneous navigation by peak. Data from TOPAZ.
Interacitve peak list visualisation in 3D. Peak table allows sorting by peak property. Selecting rows zooms to peak of interest. Data from TOPAZ.